## Slide 1
A digital twin for intelligent surfaces aided cellular network infrastructures leveraging
Intelligent Reconfigurable Surfaces
Supervisors:
Prof. Chadi Barakat
Prof. Thierry Turletti
Prof. Damien Saucez
Yaacoub YAACOUB

## Slide 2
Plan
Introduction – Motivation
IRS Working Principle
Designing Our IRS Model
Model Results
Future Work

## Slide 3
Introduction
Network deployed with higher frequencies [1]
Making the wireless environment programmable and controllable [1]
Increase spectral and energy efficiency for wireless communications [3]
Creating Virtual Line of sight between transmitter and receiver when a real LOS does not exist [2]
Main advantages of the IRS:
Reduce power transmitted by the base station [1]
Reduce the number of base stations deployed [1]
3
[2]
[1] M. Di Renzo et al., “Smart Radio Environments Empowered by Reconfigurable Intelligent Surfaces: How It Works, State of Research, and the Road Ahead,” IEEE J. Sel. Areas Commun., vol. 38, no. 11, pp. 2450–2525, 2020.
[2] Q. Wu, S. Zhang, B. Zheng, C. You, and R. Zhang, “Intelligent Reflecting Surface-Aided Wireless Communications: A Tutorial,” IEEE Trans. Commun., vol. 69, no. 5, pp. 3313–3351, 2021.
[3] H. Zhang and B. Di, “Reconfigurable Intelligent Surfaces Assisted Communications With Limited Phase Shifts : How Many Phase Shifts Are Enough ?,” IEEE Trans. Veh. Technol., vol. 69, no. 4, pp. 4498–4502, 2020.

## Slide 4
[M. Di Renzo et al., “Smart Radio Environments Empowered by Reconfigurable Intelligent Surfaces: How It Works, State of Research, and the Road Ahead,” IEEE J. Sel. Areas Commun., vol. 38, no. 11, pp. 2450–2525, 2020.
Metasurfaces Types
4
Passive Surfaces
No power amplification
Minimal digital signal processing
Minimal Power consumption for the configuration phase
Passive Reflection beamforming
Active Surfaces
Capability of generation and reception of radio signals
Requires an active RF chain per active antenna element
Active transmission beamforming

## Slide 5
“CONVERGE – Telecommunications and Computer Vision Convergence Tools for Research Infrastructures,”
A digital twin for intelligent surfaces aided cellular network infrastructures
Experimental chamber
Building a toolset combining radio and vision-based communications and sensing technologies
“view-to-communicate and communicate-to-view”
A 3D-digital twin used to validate the proof-of-concept results of experiments
5

## Slide 6
Plan
Introduction – Motivation
IRS Working Principle
Designing Our IRS Model
Model Results
Future Work

## Slide 7
Intelligent Reconfigurable Surface
Inexpensive adaptive surface
Surface divided into large number of small element
Element size < λ
Elements controlled independently
Low power usage for operation
Elements consists of Varactor Diodes or PIN Diodes
7
[3]
[2]
[1] M. Di Renzo et al., “Smart Radio Environments Empowered by Reconfigurable Intelligent Surfaces: How It Works, State of Research, and the Road Ahead,” IEEE J. Sel. Areas Commun., vol. 38, no. 11, pp. 2450–2525, 2020.
[2] X. Pei et al., “RIS-Aided Wireless Communications : Prototyping , Adaptive Beamforming , and Indoor / Outdoor Field Trials,” pp. 1–13.
[3] E. Basar et al., “Reconfigurable Intelligent Surfaces,” IEEE Access, vol. PP, no. June 2018, p. 1, 2019.

## Slide 8
IRS Main Working Principle
Changing the phase of the impinging signal to change its direction
Introducing different phase shifts to different locations of the surface
: propagation Delay
: Introduced Delay by the surface
Focusing Signal in one point: equal for all elements of the surface
8
[1] E. Bjornson, H. Wymeersch, B. Matthiesen, P. Popovski, L. Sanguinetti, and E. De Carvalho, “Reconfigurable Intelligent Surfaces: A signal processing perspective with wireless applications,” IEEE Signal Process. Mag., vol. 39, no. 2, pp. 135–158, 2022.
[1]

## Slide 9
IRS Main Working Principle
Introducing different phase shifts to different locations of the surface
Phase shifts controlled Electronically
Reflection Coefficient of one element:
  is the electrical impedance of the element
9
S. Abeywickrama, S. Member, R. Zhang, and Q. Wu, “Intelligent Reflecting Surface : Practical Phase Shift,” vol. 68, no. 9, 2020.
Notes: IRS will change the phase of the signal electronically.
The phase shift that will be introduced by each element is practically the angle of the reflection coefficient of this element.
The reflection coefficient can be calculated as follows …
It will be a complex number of the form 𝐴_𝑛 𝑒^(𝑗𝜙_𝑛 ) where 𝐴_𝑛 is the amplitude which can be thought of the attenuation coefficient of the signal. and 𝜙_𝑛 is the actual ohasse shift of the element.
So basically to control the phase shift of the element, we should be able to control the electrical impedance of this element.

## Slide 10
Varactor Model
Phase shift of an element controlled by a varying capacitance
More continuous and uniform phase shifts will be formed
Equivalent Element Impedance:
, , , are fixed values representing the physical characteristics of the element.
: angular frequency
10
[1]
[2]
[1] S. Abeywickrama, S. Member, R. Zhang, and Q. Wu, “Intelligent Reflecting Surface : Practical Phase Shift,” vol. 68, no. 9, 2020.
[2] X. Pei et al., “RIS-Aided Wireless Communications : Prototyping , Adaptive Beamforming , and Indoor / Outdoor Field Trials,” pp. 1–13.
Notes: electrical impedance of the element will depend on the electronic model of the element
One possible model will be using varactors.
Varactors are electronic components capable of changing its capacitance based on different bias voltages.
For varactor model, the reflecting element can have the following model shown in the figure .. and the equivalent impedance is calculated as follows 𝑍_𝑛 …
Where 𝑅_𝑛, 𝐿_1, 𝐿_2, are fixed values representing the physical characteristics of the element.

## Slide 11
Varactor Model
11
[1]
[1] X. Pei et al., “RIS-Aided Wireless Communications : Prototyping , Adaptive Beamforming , and Indoor / Outdoor Field Trials,” pp. 1–13.

## Slide 12
Plan
Introduction – Motivation
IRS Working Principle
Designing Our IRS Model
Model Results
Future Work

## Slide 13
Designing Our IRS Model
Inputs:
  Transmitter coordinates
  Receiver coordinates
  Transmitted Signal
  Carrier Frequency f (in Hz)
  Amplitude A_i (in V)
  Phase φ_i (in rad)
Outputs:
  Phase shift of every element of the IRS
  The power received
13

## Slide 14
Designing Our IRS Model
Generalized Snell’s Law of Reflection:
Noting that the phase shift gradients should always be in the [-π π] range
Estimate the function from derivatives and
14
[1]
[1] N. Yu et al., “Flat Optics : Controlling Wavefronts With Optical Antenna Metasurfaces,” vol. 19, no. 3, 2013.
Notes: As we explained earlier, the reflection will follow the modified snell’s law which is defined by these 2 formulas.
This law will combine incident and the reflection angles of the signal with the gradient of the phase shift of the surface.
Knowing that we can geometrically calculate the incidence angle 𝜃_𝑖, the reflection angle 𝜃_𝑟 and the deviation angle of the reflected vector from the incident plane 𝜑_𝑟 since we already know the locations of the receiver and the transmitter and the location of the surface on a predefined 3D space.
Using snell’s formula, we will calculate the needed gradient phase shift in both x and y directions in order to achieve the required reflection.
Then we will estimate the required phase shift based on its gradients.to do this we should assume a starting phase and calculate the phase shift accordingally. We should note here that calculating the phase shift from its gradient on the x direction or y dierection should have the same answer, but since we are estimating the starting point, minor errors could be introduced so the reduce these errors the final phase shift will be calculated by taking the average of both phase shifts calculated in the x and the y directions.

## Slide 15
Designing Our IRS Model
15
[1]
[1] N. Yu et al., “Flat Optics : Controlling Wavefronts With Optical Antenna Metasurfaces,” vol. 19, no. 3, 2013.

## Slide 16
IRS Model Validation
Estimate the Capacitance needed from the varactor
Calculate back the real phase shifts implemented on the surface
16

## Slide 17
IRS Power Model
Using Friis transmission equation.
Assuming no direct line of sight between the Transmitter and the receiver
Adding up at the receiver location the power collected by each element, while removing erroneous reflections
17

## Slide 18
IRS Power Model
18
Notes: As expected, increasing the number of elements ill increase the power received.
But increasing the number of elements indefinitely will not keep increasing the received power.
If N goes to infinity 𝑥_𝑛+𝑥_𝑛^′ which are the distances between the transmitter and the surface, and the surface and the receiver will also tend to infinity which mean the second part of the summation will tend to 0. therefore, the above a certain threshold the additional elements to the surface will stop effectively contributing to the signal reflection

## Slide 19
IRS Model Results
19

## Slide 20
IRS Model Results
20

## Slide 21
Future Work – Modeling PIN Diode Model
21
[2]
[1]
[1] H. Yang, X. Cao, F. Yang, J. Gao, S. Xu, and M. Li, “OPEN A programmable metasurface with dynamic polarization , scattering and focusing control,” Nat. Publ. Gr., no. October, pp. 1–11, 2016.
[2] R. Fara, P. Ratajczak, A. Ourir, M. Di Renzo, and J. De Rosny, “6G : THE PARADIGM FOR FUTURE WIRELESS COMMUNICATIONS A Prototype of Reconfigurable Intelligent Surface with Continuous Control of the Reflection Phase,” no. February, pp. 70–77, 2022.

## Slide 22
Thank You
22

## Slide 23
[1] R. Fara, P. Ratajczak, A. Ourir, M. Di Renzo, and J. De Rosny, “6G : THE PARADIGM FOR FUTURE WIRELESS COMMUNICATIONS A Prototype of Reconfigurable Intelligent Surface with Continuous Control of the Reflection Phase,” no. February, pp. 70–77, 2022.
PIN Diode Model
Discrete phase shifts based on diodes states
Discrete elements impedance values, depending on the element architecture and diode state
23
[1]

## Slide 24
PIN Diode Model
24
[1]
[1]
[1] R. Fara, P. Ratajczak, A. Ourir, M. Di Renzo, and J. De Rosny, “6G : THE PARADIGM FOR FUTURE WIRELESS COMMUNICATIONS A Prototype of Reconfigurable Intelligent Surface with Continuous Control of the Reflection Phase,” no. February, pp. 70–77, 2022.